## Slide 1: A Decentralized Multi-Robot Task Allocater based on robot resources.
Shailendra Sekhar Bathula

## Slide 2: CONTENTS
Introduction
System Architecture
Algorithms
Videos
Conclusion

## Slide 3: INTRODUCTION
Task Allocation
Auction Based Task Allocation
Taxonomy of the project
  ST-SR-TA
Resources
Project Description
  Build a task allocator which considers the resources of the robot.

## Slide 4: SYSTEM ARCHITECTURE
Winner Update
Process
List Update
Process
Bid Generator
Process
Task Trade
Process
ROBOT
OUTPUT
INPUT

## Slide 5: ALGORITHMS
Winner Update
Bid Generator
Task Trade
List Update

## Slide 6: Winner Update Process
BID LIST
TRADE LIST
BID LIST
[TASK ID , ROBOT ID , BID , AUC]
TRADE LIST
[BEST CANDIDATE, BID , RESOURCE, PRIORITY, AUC]

## Slide 7: Winner Update Process
No information about the task in the trade list
Message from auctioneer  TRUE
Have information about this task in our trade list
Bid (message) < bid (trade list)
Update Trade List

## Slide 8
BID GENERATOR (New Task)
Checks if the message from the robot itself
The bid calculated is less than the bid from the message
Update Trade List
No information about the task in the trade list
Message from auctioneer  TRUE

## Slide 9: Bid Generator
Bid Calculation
  Bid is the distance required to travel in order to complete the task
Priority Calculation
  Priority for the task
Resources after the task is complete
  Resource depletion is directly proportional to the distance traveled

## Slide 10
Bid Generator (new task)
Task Threshold
No tasks previously
allocated
Previously Allocated tasks
Direct = Distance(robot, new task)
Indirect = Distance(robot, charging station)
+ Distance(new task, charging station)
Check Battery = Current Battery - Direct
Bid = Direct
Battery after task =
Current Battery - Distance
Bid = Indirect
Battery after task =
Max Recharge – task threshold
Direct = Distance(old task, new task)
Indirect = Distance(old task, charging station)
+ Distance(new task, charging station)
Check Battery = Current Battery - Direct
Bid = Direct
Battery after task =
Current Battery - Distance
Bid = Indirect
Battery after task =
Max Recharge – task threshold
Check if the bid calculated < the bid of the old task
Priority for the new task = Index of old task
> Threshold
< Threshold
> Threshold
< Threshold
Yes
No
Old task

## Slide 11: Task Trade Process
Identify the best task for the robot
The robot is the auctioneer, then let others know who the winner of the task is

## Slide 12
Task Trade Process
Check if best task is known
Task with the minimum bid from trade list from tasks of the robot
Send a new bid vector to check if others have lower bids, if not proceed
The task is originally of the robot
- Update Best Task
The robot is auctioneer, create a message and send to neighbors who the winner is, for the winner to accept it and others reject it
No
Yes
Wait some time for responses

## Slide 13: List Update
Task per robot
  Tasks allocated to robot
Bid per task
  Bid of the tasks allocated to the robot
Battery after task
  Battery after task for tasks allocated to the robot

## Slide 14
List Update
Best task
Dummy bid vector to the bid list
Insert data of best task into our lists in priority
Status = Perform
Current task
- Allocate the first task in task per robot as the current task
Current task complete
Remove details about the task completed
Set current task = 0
Status = Refill
Set current task = 0
Create bid vector messages about each task in the list and send it to the bid list
Clear all lists

## Slide 15: Live Demos

## Slide 16: CONCLUSION
Implemented a decentralized auction-based algorithm considering resources.
Comparison with a centralized system.
Future work: Modular programming for each robot separately and monitor communication delays.